## Slide 1: Introduction to Seismology
CIDER 2014
Seismology Lecture #1
Ved Lekic
University of Maryland
geol.umd.edu/~ved

## Slide 2: What is seismology?
Seismology is the study of the generation and propagation of elastic waves
Study of wave generation is termed source seismology:
  Earthquakes
  Tremor / micro-seismicity associated with hydrofracturing
  Explosions / mine collapses
  Ocean-solid-Earth interactions
Study of wave propagation can be used to infer properties of the inaccessible interior of objects – structural seismology:
  Oil / gas / mineral exploration
  Mantle tomography
  Converted wave imaging
  Waveform modeling

## Slide 3: What are elastic waves?
In an elastic continuum, perturbing the position of one particle will result in a restoring force that will accelerate that particle back and past the equilibrium position
Perturbation in position of one particle will accelerate its neighbors
Amplitude
Distance
Period =
Frequency -1
T = 1/f
Wavelength = Wavenumber-1
λ= 1/k
Speed (c):
c = λf = f/k

## Slide 4: Frequencies / Periods of motion
Seismology spans ~6 orders of magnitude in frequency, from waves that oscillate >1000 times in a second, to those that take >1000 seconds to oscillate once
From Stein and Wysession, 2003

## Slide 5: Tractions and the stress tensor
The stress tensor describes forces acting across infinitesimal planes within a continuum (i.e. tractions)
Its units are: N/m2 a.k.a. Pa
Can vary with position, describes both compression / estension and shearing
Stress tensor is symmetric, in 3D has 6 independent components
Gravity:
direction always down
Pressure:
direction depends on surface

## Slide 6: Internal deformation
How do we describe (small) internal deformations?

## Slide 7: Strain and Rotation tensors
No net rotation only if ∂ui/∂xj – ∂uj/∂xi = 0
Decompose deformation into Strain and Rotation matrices:
                +
Strain is a dimensionless quantity (ΔL/L )
Strain due to passage of seismic waves are typically <10-5
Strain tensor is symmetric
Rotation tensor is anti-symmetric

## Slide 8: Constitutive relationship
In an elastic medium, stress and strain are linearly related (for small strains, and assuming perfect elasticity)
In 1D, this is the familiar Hooke’s Law:
F = - k x
The constant k is the spring stiffness
In 3D, x becomes the strain tensor, and F becomes the stress tensor:

## Slide 9: Elastic tensor and anisotropy
The 4-th order tensor relating stress to strain has 81 components (3 × 3 × 3 × 3 = 81) with units of pressure (GPa)
Because of symmetry of stress and strain tensors internal deformation energy considerations, cijkl = cklij = clkij = cklji 21 independent components
Specifying all 21 at every point is needed in a medium with general anisotropy
To zeroth order, Earth is isotropic at large scales: only 2 independent components (Lamé parameters):

## Slide 10: Isotropic medium representations
In an isotropic medium, wave speed depends on NEITHER the direction of propagation NOR polarization direction
Relationship between stress and strain is simple:
Shear modulus: measure of the resistance of material to shear.
Bulk modulus: measure of incompressibility of a material. Given by hydrostatic stress divided by fractional volume change.
Poisson’s ratio: lateral contraction of a cylinder divided by longitudinal extension.

## Slide 11: Momentum  Seismic Equation
Homogeneous momentum equation governs seismic waves outside of source regions
Summation convention: repeated index  summation, e.g. ekk = e11 + e22 + e33.
Constitutive relation for isotropic medium, where we used 2ejk = (∂uk/∂xj + ∂uk/∂xj)
Seismic Wave Equation for an isotropic medium
+ manipulation and a vector identity:

## Slide 12: Seismic Wave Equation
Divergence: Scalar describing volume change
Curl: Vector describing infinitesimal rotation (think paddle wheel)
Gradient: Vector describing the direction and magnitude of change in a quantity

## Slide 13: Homogeneous medium
In a homogeneous medium, or in the high-frequency approximation, the gradients of λ and μ can be neglected:
Taking the divergence of the equation (remember ):
Taking the curl of the equation (remember and ):
Compressional wave (P-wave) propagating at speed α
Shear wave (S-wave) involving no volume change propagating at speed β

## Slide 14: P and S waves
http://www.geo.mtu.edu/UPSeis/images/
P waves: volume & shape change, particle motion in the direction of propagation
S waves: only shape change (no volume change), particle motion perpendicular to direction of propagation
  SH – particle motion in the horizontal plane
  SV – particle motion in the vertical plane

## Slide 15: Plane waves
Solutions to the P and S equations are waves: u(x,t)= f(x ± vt), v = velocity
Plane waves:
  s is the slowness vector
Particle displacement at a frequency ω:
  k is the wavenumber vector
(Figure from Stein and
Wysession, 2003)

## Slide 16: Horizontal & vertical slownesses
We can measure how quickly a wave sweeps across a small, dense array of seismometers
Slowness: u = 1 / c
Horizontal slowness: p = ΔT/ΔX
Vertical slowness:
figures from Shearer, 2009

## Slide 17: Snell’s Law – the ray parameter
For wavefield to remain continuous along interface between regions with different velocities, waves will change direction in addition to their speed.

## Slide 18: Snell’s Law – the ray parameter
Snell’s Law:
Ray parameter (horizontal slowness) remains the same along the ray path
For wavefield to remain continuous along interface between regions with different velocities, waves will change direction in addition to their speed.
figure from garnero.asu.edu

## Slide 19: Layered / shell medium
By specifying a ray parameter and a starting location, we fix the ray-path through a layered or spherically-symmetric Earth
The deepest depth the ray can reach is one where:
figure from garnero.asu.edu

## Slide 20: Travel-time curves
T(X) = τ(p) + pX
Ray parameter (horizontal slowness) is the slope of the travel-time curve
Different rays observed at different distances
Shallowing of slope dT/dX with distance  slowness decreases with depth
figures from Shearer, 2009

## Slide 21: Seismic wavefield
P waves
S waves
Seismic waves take a variety of paths and sample all parts of the Earth
They provide most complete and direct information on present-day state of the deep interior

## Slide 22: Wavefronts and raypaths

## Slide 23: Ray nomenclature
Moho
figures from Shearer, 2009

## Slide 24: Earth’s 1D (radial) structure
A number of 1D Earth models have been developed: PREM (Dziewonski and Anderson, 1981), ak135 (Kennett et al., 1995), IASP91 (Kennett and Engdahl, 1991).
Seismically fast lithosphere
Seismically slow asthenosphere (LVZ)
Velocity jumps at 410 and 660 km define the transition zone from the upper and lower mantle
CMB is at ~2891 km depth
ICB is at ~5150 km depth

## Slide 25: Body wave observations
figures from Shearer, 2009

## Slide 26: Triplications
Depth ranges in which velocity increases rapidly with depth can produce triplications: multiple rays (with different horizontal slownesses) arrive at the same time
Transition zone discontinuities produce triplications
At epicentral distances > 30° rays bottom in the lower mantle and no triplications are (typically) observed
figures from Shearer, 2009

## Slide 27: Shadow zones
Shadow zones
Rays cannot bottom in a depth range where velocity decreases with depth*
Low-velocity zones produce shadow zones
Prominent shadow zone in PKP waves due to low velocities in the outer core
figures from Shearer, 2009

## Slide 28: Shadow zones
Shadow zones
Rays cannot bottom in a depth range where velocity decreases with depth*
Low-velocity zones produce shadow zones
Prominent shadow zones result from low velocities in the liquid outer core
P waves
S waves

## Slide 29: Surface wave observations
figure from Stein & Wyssession, 2003

## Slide 30: Relationship to body waves
Love waves
Constructive interference between surface-bouncing SH waves
Rayleigh waves
Constructive interference between post-critically reflected P and SV waves
figures from Shearer, 2009

## Slide 31: Surface waves
Love Waves
Particle motion is in the horizontal plane perpendicular to direction of propagation
Rayleigh Waves:
Particle motion is confined to the vertical plane joining source-receiver.
figures from Shearer, 2009

## Slide 32: Surface waves
Love Waves
Particle motion is in the horizontal plane perpendicular to direction of propagation
Rayleigh Waves:
Particle motion is confined to the vertical plane joining source-receiver.
http://www.geo.mtu.edu/UPSeis/images/

## Slide 33: Phase vs Group velocity
When different frequencies propagate at different (phase) velocities, packets of seismic energy travel at a different velocity (group)
Phase velocity: c = ω/k
Group velocity: U = dω/dk
Group velocity is always slower than phase velocity
At high frequencies, it is easier to measure group velocities since measuring phase velocities has the potential for cycle skipping
figures from Shearer, 2009

## Slide 34: Measuring dispersion
By filtering a seismogram to include waves of different frequencies, we can measure the phase and group velocities as a function of frequency
Longer period waves “feel” deeper in the earth than shorter period waves
Longer period surface waves travel faster  velocity increases with depth
figures from Shearer, 2009

## Slide 35: Love & Rayleigh Dispersion
At periods where group velocity attains a maximum or minimum, large amplitude surface waves are seen  “Airy” phases
figures from Shearer, 2009

## Slide 36: Signature of plate cooling
Phase velocity measurements of Rayleigh waves allowed seismologists to infer how velocities increase with plate age (colder temperatures  faster velocities)
(Figure from Stein and
Wysession, 2003)

## Slide 37: Exploiting ambient noise
Impact of ocean waves on the shores (primary microseism) and pressure variations on the ocean floor due to ocean waves (secondary microseism) create Rayleigh waves that propagate around the Earth in all directions
By computing cross-correlations of noise at pairs of seismometers we can extract and measure Rayleigh wave dispersion
These measurements can be used to image the Earths’ interior (ambient noise tomography)
Shapiro & Campillo 2004

## Slide 38: Lateral variations in structure
We can infer 3D velocity distribution using:
  Absolute and differential travel-times measured across many different paths
  Similarly, phase / group velocity measurements at different frequencies and on different paths
  Directly analyzing full waveforms recorded on different paths
French et al. 2013

## Slide 39: Amplitudes - Relative
So far, we have just discussed travel times of waves through the Earth (only depend on velocity)
What factors cause amplitudes to change as waves propagate?
  Reflection / transmission coefficients
  Geometric spreading
  Scattering / redistribution of seismic energy
  Focusing / defocusing by structure
  Intrinsic attenuation

## Slide 40: Reflection/transmission coefficients
Impose continuity of displacements and tractions across solid-solid interface
R/T coefficients depend on impedance: the product of velocity with density
α1, β1, ρ1
α2, β2, ρ2
figures from Shearer, 2009

## Slide 41: SS and PP precursors (reflection)
SS (or PP) precursors are waves reflected from a discontinuity in the subsurface and observed before the arrival of the surface-reflected wave
Their amplitude (as a function of epicentral distance) can constrain both Vp, Vs and density jumps across mantle discontinuities!
Figure by Schmerr

## Slide 42: SS precursors (reflection)
SS (or PP) precursors are waves reflected from a discontinuity in the subsurface and observed before the arrival of the surface-reflected wave
Their amplitude (as a function of epicentral distance) can constrain both Vp, Vs and density jumps across mantle discontinuities!
http://terpconnect.umd.edu/~nschmerr/Research.html

## Slide 43: Receiver Functions (transmission)
α1, β1, ρ1
α2, β2, ρ2
P-waves from distant quake
S-waves converted across interface
Teleseismic waves can convert from P-to-S or S-to-P beneath a seismometer
Relative timing between P(S) and Ps(Sp) arrivals constrains the depth of the interface
Relative amplitude of P/Ps and S/Sp constrains impedance contrast across interface
H
TP – TPs = H (ηS – ηP)

## Slide 44: Focusing by slow anomalies
Transverse-component velocity waveforms from the 4/11/2010 Spain event
Stations in 91º -102º epicentral distance range  S waves grazing the core-mantle boundary
S/Sdiff waveforms show amplitude focusing and travel-time delays
Lekic et al. EPSL 2012
FOCUSING

## Slide 45: Seismic attenuation
Focusing/Defocusing
Scattering
Extrinsic attenuation
incoming elastic energy
is conserved
Intrinsic attenuation
incoming elastic energy
is transformed
Geometrical spreading
Anelasticity
(dislocations, diffusion, … )
Karato & Spetzler [1990]
Q (quality factor) or q (absorption)
q = 1/Q = - DE/2pE = - DA/pA

## Slide 46: Scattering
Seismic waves can scatter from heterogeneities within the elastic medium
Scattering is efficient if the size of the scatterer is similar to the wavelength
Scattering re-distributes energy, decreasing amplitudes at the beginning of a seismogram, and increasing them in the back (the “coda”)

## Slide 47: Characterization of intrinsic attenuation
external gradient
Elastic energy of waves is consumed in dissipative processes (Knopoff, 1964)
Many different dissipation mechanisms exist in the mantle
(e.g. Jackson and Anderson 1970)

## Slide 48: Characterization of intrinsic attenuation
external gradient
Incident seismic wave
Elastic energy of waves is consumed in dissipative processes (Knopoff, 1964)
Many different dissipation mechanisms exist in the mantle
(e.g. Jackson and Anderson 1970)

## Slide 49: Characterization of intrinsic attenuation
external gradient
Incident seismic wave
Elastic energy of waves is consumed in dissipative processes (Knopoff, 1964)
Many different dissipation mechanisms exist in the mantle
(e.g. Jackson and Anderson 1970)
energy cost G(P,T,x)
= attenuation

## Slide 50: Characterization of intrinsic attenuation
Often assumed thermal activation
Frequency dependence
external gradient
energy cost G(P,T,x)
= attenuation
Incident seismic wave
Global entropy increase
Elastic energy of waves is consumed in dissipative processes (Knopoff, 1964)
Many different dissipation mechanisms exist in the mantle
(e.g. Jackson and Anderson 1970)

## Slide 51: Dispersion due to attenuation
Because they have more oscillations per unit distance, higher frequencies are more attenuated
If all frequencies travelled at the same speed, then causality would be violated
Low frequency waves are slowed down more than high frequency waves
figures from Shearer, 2009

## Slide 52: Earth attenuation structure
Dziewonski & Anderson (1981)
Widmer et al. (1991)
Durek & Ekström (1996)
Lawrence & Wysession (2006)
Hwang & Ritsema (2011)
figure by Matas

## Slide 53: Frequency dependence
Q depends on frequency
Q is frequency independent
Lekic et al., 2009
figure from Shearer, 2009

## Slide 54: Amplitudes - absolute
To get at absolute amplitudes, we have to consider the seismic source
Can an earthquake be represented by a single body force?
To conserve both linear and angular momentum (no net acceleration, no net torque), body forces representing earthquake sources must appear in pairs of force couples (a.k.a. double couples)

## Slide 55: Double-couple mechanisms
μ – rigidity of rock
D – average slip on fault
A – area of that slipped

## Slide 56: Radiation from moment tensors

## Slide 57: P-wave radiation pattern
P-wave amplitude is:
Most positive in the direction of the tension axis
Most negative along compression axis
Zero along primary and auxiliary plane directions

## Slide 58: S-wave radiation pattern
S-wave amplitude is:
Greatest along primary and auxiliary plane directions
Particle motions are away from P-axis and toward T-axis

## Slide 59: Beach-Balls
We can graphically represent a moment tensor by shading areas where first-arriving P wave would be positive  “beach-ball” representation
Extend along shaded portions, compress along unshaded

## Slide 60: Centroid Moment Tensors
“Harvard” CMT (Dziewonski & Woodhouse, 1983): www.globalcmt.org

## Slide 61: Conclusions
Seismology is a big field!
Questions?